AiS simple? Not for me. 

Got an old ICOM FS3 with the two AIS freq programmed in by supplier(its a DOS programable commercial handheld).
Found the discriminator and taped it similar to the www.discriminator.nl suggestion (site recommended by Idnd and I concur)

Intalled and attempted to run gnuais. Wouldn't run due to the logging paths not set. Finally got it working by commenting out the 'offending' bits in the code however no output. (Hackoon has subsequently enlightened me further) Is it the radio or software? 

Spent some time with both Soundmodem (has a fsk but no gmsk decoder ) and XOscope (poor mans soundcard oscilloscope)  to see if I could find the ais modulation at least visually. I thought it was a good one with repeating signal (subsequently discovered the radio must be intermittantly turning off and on to conserve power so what I thought a good signal wasn't after all). 

Got desperate so loaded up Shipplotter in wine -I use Ubuntu but SP installed OK . Ran the diagnostic and got a bit of a signal displayed. Over an hour or so  I managed to obtain only two ais transmissions . Unfortunately havent been able to repeat. At least it gave me hope to contine but -Is it the radio or software? 

Well, I had my boat VHF- a Uniden MC610 which is rather ancient with discrete components and with no  circuit diagram for it. I traced the circuit using superimposed camera images in Gimp of the top and btm of circuit board and found a likely looking discriminator site. Turned out I was right and even downloaded the chip datasheet. From that I am reasonably confident I tapped the right point with the requisite? 10k resistor. Fired up the software but no output with the radio tuned on channel 87. Is it the radio or software?

Wasnt sure I was receiving the 87/88 duplex channel or the newer 87/88 simplex channel (which apparently changed on post 2004 build vhf radios) WARNING Check out www.discriminator.nl site to see if you can receive ais on ch 87 88 as Hackoon suggested. Also used the ICOM to transmit 161.975 and was received OK on the  MC610 so its confirmed at least it is tuned in. Is it the radio or software?
 
Thought of gnuradio. Installed and ran the audiofft.py program which I used as diagnostic. I was attracted to the waterfall display but could only manage the fft and scope displays. The waterfall dispaly wouldnt work but I gather this is a new beta feature. The fft showed modulation spread 0-12k which I thought reasonably despite reading that the ais bandwidth can be 12 or 25kHz. However I accidentally tuned to another channel and got the same similar output. The penny dropped that what I was looking at was probably noise and not signal! I then transmitted a voice tone on one radio and received it on the other. The modulated output as it appeared on XOscope was smaller than the 'noise trace' which confirmed my suspicion. Is it the radio or software? Probably the radio!

For an antenna I was using a 88-108FM 1/4 wave dipole above the roof -no not on the boat- and I also tried the TV antenna with its masthead amplifier. I'm only located 10 mile away from shipping activity so I thought I should be receiving OK even if side lobed. Since I need a new antenna on the boat anyway I'll now make a J pole antenna and try that (The advantage of this is it has basically a grounded feed point which will make the radio  much more resistant to lightning strike -better than the present dipole now atop the mast - I plan to afix it to the back stay on a 'slide' with feed cable clipped to the same stay which will enable me to 'hoist it' up and down for servicing). 

Perhaps another new radio or NASA ais engine or similar? I'd like to resist the latter and continue with  diy having spent so much effort todate.   
I also have an ICOM M9 handheld which should also work but I'm reluctant to meddle as it is so compact and I dont have circuit diagram. Probably will try and pickup a secondhand hand scanner radio.














I eventually got it working by commenting out the "offending code bits". Help provided by Hackoon will assist next time.