Am I ready Checklist

If you can answer YES to every item on this list, your boat is ready to go cruising and so are you…

# Hull:

All through hulls removed, inspected, replaced as necessary, and rebidded

Rudder removed, all bearings inspected , replaced as necessary and rebidded and refastened

All sea cocks removed, inspected, replaced or lubricated as necessary, rebidded and refastened.

Cutlass Bearing replaced and rebidded.

Stuffing box removed, inspected, replaced as necessary, repacked with Teflon packing, reinstalled with new hose and hose clamps.

Propellor shaft removed, inspected, replaced, and aligned as necessary.

Propellor removed, inspected and replaced as necessary.

Mast step inspected, and refurbished as necessary.

Bonding straps inspected and replaced as necessary, with all connections refurbished.

Keel bolts if present removed and replaced  with new ones properly bedded.

Bulkheads inspected to ensure all are properly bonded to the hull, and rebonded as necessary..

Hull deck joint refastened and rebedded or sealed with multiple layers of GRP tape.

# DECK:

Hull deck joint refastened and rebedded  or sealed with multiple layers of GRP tape.

All stanchion bases, including those for the pulpits and pushpits, removed, inspected, and rebedded and refastened to foundations rebuilt as necessary so the core in cored decks is hardwood, and the fastenings go entirely through the deck and into backing plates at least as large as the bases themselves.

All cleats removed, refastened and rebedded.

All portlights removed, refastened and rebedded.

All hatches removed, refastened and rebedded.

All track removed, refastened, and rebedded.

All winches  removed, serviced, refastened, and rebedded.

All hinges and other deck hardware not mentioned before, removed, replaced as necessary, refastened and rebedded.

# MAST:

All cleats removed, refastened and rebedded.

All wiring removed, and replaced.

All Mast steps removed, inspected, replaced as necessary, rebedded and refastened.

All tracks removed, refastened, and rebedded.

All winches removed, serviced, refastened, and rebedded.

All tangs removed, refastened and rebedded.

All spreaders removed, refastened, and rebedded.

All lights removed, serviced, refastened, and rebedded.

Gooseneck, disassembled, inspected for wear and serviced or replaced as necessary.

# BOOM:

All cleats removed, refastened and rebedded.

All tracks removed, refastened, and rebedded.

All winches removed, serviced, refastened, and rebedded.

All tangs removed, refastened and rebedded.

# STANDING RIGGING:

All wire older than 10 years reterminated  or replaced.

Bobstay if present, replaced.

All rigging pins older than 10 years, replaced.

All rigging screws of closed type, or of stainless construction replaced with open barrel bronze screws.

All toggles, shackles, link pins, link plates, diamond plates, and other rigging hardware, removed, inspected, and replaced as necessary, with all pins or bolts replaced outright.

All tangs removed, inspected, replaced as necessary, rebedded and refastened.

All chainplates removed, inspected, replaced as necessary, rebedded and refastened.

# Running Rigging:

All halyards and sheets which show hardening from the sun replaced.

All blocks removed, serviced as necessary, and or replaced, including masthead sheaves…

All winches removed, serviced, refastened, and rebedded.

ANCHOR:

Chain regalvanized, and end for ended as necessary, or replaced as necessary.

Pawl installed or serviced.

Anchor chock modified so it is closed, or can be closed.

Anchor roller removed, inspected, refastened and rebedded as necessary.

Spare anchors properly chocked on deck and below.

# SAILS:

All sails opened, inspected, replaced if they fail the poke test, restitched, patched, and cleaned as necessary.

All sails set to verify sheet leads and fit.

# RUDDER:

Rudder removed, bearings, or gudgeons and pintles,  removed, inspected rebedded, and replaced as necessary.

Cable for cable steering replaced.

Tiller removed, inspected, and replaced as necessary.  Spare tiller stowed together with spare tiller fitting for rudder stock.

Hydraulic steering inspected for leaks, which are fixed, generally via replacement of defective components.  Cylinder rebuilt.  Helm pump rebuilt, control valves removed,  inspected and refurbished or replaced as necessary..

# GALLEY:

Cooker opened, inspected and defective parts replaced as necessary.

Sink, removed, inspected for excessive thinning due to corrosion, replaced as necessary, rebedded and refastened.

All plumbing replaced with new.

All pumps removed, inspected, and refurbished or replaced as necessary.

Insulative capacity of ice box or refrigerator assessed via the ice block test, with insulation replaced if test fails

Refrigeration system inspected, checked for leaks, and refurbished as necessary.

# EMERGENCY RESPONSE EQUIPMENT:

Fire extinguishers serviced and mounted in strategic locations.

Flares examined, and sufficient purchased which are in date, to  meet regs.

PFDs inspected and sufficient maintained aboard to provide each crew member with a serviceable unit.

All PFDs equipped with strobes, and whistle

Bosn’s chair inspected and refurbished as necessary.

Safety harnesses, inspected and refurbished as necessary.

Throwable PFD, (horseshoe ring, lifering, lifesling) inspected, strobe verified as working, line verified to be in good condition, and mounting verified to be solid and to permit rapid access and deployment.

# ENGINE:

All zincs removed, inspected, and replaced as necessary.

Impellor replaced.

Oil changed.

Compression checked, and engine problems assessed; if check fails, defective items refurbished as needed.

Injectors refurbished.

Inspect engine mounts, refurbish or replaced as necessary.

Injection pump refurbished as necessary

# GEARBOX:

Oil changed.

Operation checked, with special emphasis on slippage, if found, replace clutches.

If leaks are found, replace seals.

If rear seal leaks, suspect improper shaft alignment.

Align propeller shaft.

# Navigation:

Navigation skills appropriate for the voyage have been acquired via coursework or self study, including coastwise piloting, dead reckoning, speed estimation, deck log entries, celestial navigation, weather prediction, and tide and current prediction.

Pilots and pubs covering the area to be cruised are aboard, including:

BA pilots covering the area, cruising guides covering the area.

Admiralty List of Radio Signals(Vol 3(2) for the Americas for met broadcasts

Admiralty Light List for the area

Admiralty tide tables for the area.

Nautical Almanac covering the time of the cruise

Charts or facsimiles thereof covering the area to be cruised.

Duttons or Bowditch

Plotting sheets

Weems Plotter

Dividers

Pencils

Pens

Log book

Hand held VHF or VHF

Grundig or similar HF receiver.

# SPARES:

Sufficient spare parts are aboard to maintain the critical systems of the ship at sea, including:

Spare line

Spare blocks

Sail repair kit

Engine oil and filters

Fuel filters

Spare set of Injectors, with copper washers and torque wrench.

Cable cutter capable of cutting the largest rigging wire on the boat, and the anchor chain.

Hack saw

Hammers

Drill and bits

Wrenches

Screw drivers

Come along

Axe

Panga

A spare piece of rigging wire sufficiently long to replace the longest stay on the boat, with one end terminated, and a staylock or other field installable terminal for the other end.

Hose clamps

Hose

Hose fittings

# WATER:

Sufficient water storage capacity in tanks, jugs, or bladders available below decks to provide each crew member with 1 gallon per day over the longest passage envisioned.

# DINGHY:

A hard dinghy of sufficient size to carry the entire crew and emergency provisions, including water, and emergency navigation equipment, including sextant and compass and charts, with a set of oars for each man, and preferably with a sailing rig, to provide means of escape in the event of sinking, and assess to shore when in port.

Chocks and padeyes, and ratchet tiedowns to secure the dinghy on deck.