SECTION 1: GENERAL CONDITIONS

CONTENTS

1.01		INTENT

1.02		DEFINITIONS

1.03		AGREEMENT CONDITIONS

1.04		PLANS AND SPECIFICATIONS

1.05		WEIGHT CONTROL

1.06		REQUIRED OWNER'S DECISIONS

1.07		ALTERATIONS AND EXTRAS

1.08		OWNER'S ITEMS

1.09		INSURANCE

1.10		CARE OF THE YACHT

1.11		SHOP PRACTICE

1.12		CONTRACT DRAWINGS

1.13		PLANS AND DRAWINGS

1.14		CLASSIFICATION AND CERTIFICATES

1.15		GENERAL COND./CONST. AND DELIVERY

1.16		MATERIALS AND WORKMANSHIP

1.17		PROGRESS SCHEDULE AND PHOTOGRAPHS

1.18		QUALITY CONTROL

1.19		TESTS DURING CONSTRUCTION

1.20		LAUNCHING PROCEDURE

1.21		DOCK TRIALS

1.22		SEA TRIALS

1.23 		INCLINING TEST

1.24		DELIVERY AND HANDOVER

1.25		OPERATION AND MAINTENANCE MANUALS

1.26		SPARES AND TOOLS

1.27		DOCUMENTATION

1.28		PRICE ALLOWANCE/OWNER'S SUPPLIES/

DESIGN FEES

1.29		DESIGN MODEL

1.30		MOCK-UPS

1.19		TESTS DURING CONSTRUCTION

All inspections, tests and trials are to be held under the direction and supervision of the BUILDER and will be conducted in accordance with the requirements of the Classification Society and other regulatory bodies and with the prior agreement of, and to the satisfaction of, the OWNER and Owner's Representative.

The Owner's Representative will attend all inspections, tests and trials within the BUILDER's yard and at the subcontractors premises.  Proper notice of all such test, inspections and trials, including but not limited to the Dock Trials and the Sea Trials, will be given by the BUILDER.

The Builder will keep records of the results of all     inspections,tests and trials, together with all appropriate certifications.  Prior to delivery of the Yacht, the BUILDER will prepare a detailed booklet of all such records and certificates and will submit the same in triplicate to the OWNER.

Inspections and tests will be conducted on all fabrications, machinery, equipment and fittings, etc. during all phases of the construction process by the Classification Society, in accordance with their requirements, in order that the desired class notation may be obtained.

All steel and aluminium structures will be inspected and the watertight testing of all tanks, bulkheads, superstructures, decks and wet spaces will be carried out.  All tanks will be pressurized prior to final weld coating in accordance with the requirements of the Classification Society.

Areas required to be weather tight, such as hatches, doors, windows and sidelights etc. will be thoroughly hose tested by pressure jet before Dock Trials and Sea Trials.

All requirements of the Classification Society regarding construction tests and x-ray testing are to be carried out.  The BUILDER will comply with additional x-ray testing of welded joints that may be requested by the OWNER or the Owner's Representative which is in excess of the requirements of the Classification Society.

The Classification Society may have tensile tests taken of the steel to be used in the construction of the Yacht at the expense of the BUILDER.  The Classification Society has the right to reject any material that does not meet with its requirements.

The BUILDER will furnish competent personnel to obtain and record necessary data in machinery spaces and on deck, and will supply all necessary gauges, thermometers, and/or portable instruments to accomplish these tasks.

All data obtained during tests or trials, including Dock Trials and Sea Trials, are to be accurately tabulated and delivered in triplicate to the Owner's Representative and the Naval Architect.