This document is a guide for qualified users.  The authors are not responsibility for the consequences of installation errors.

# Text boxes

Modification of Yanmar 3GM Start Circuit

2/11/09

Fuse

Start

button

Automotive type relay:

Rating: 12 volt DC, 40 amps.

85

7

Engine

Battery 12 V

867

87

New Relay Contacts

Engine starter

30

87

Boat solenoid contacts

Boat solenoid coil

New Relay Coil

Ground to

engine block

Existing start solenoid white wire

Existing Yanmar components

New components and wiring

The required new relay is a type easily available at automotive stores and Radio Shack.  Consider Optronics A-715 for less than $5 at Advance Auto Parts.  An advantage of purchasing this same relay is that the terminal numbers match the drawing above.  However, those terminal numbers may be standard in the automotive industry.

To minimize the effect of engine vibration on the new relay, the authors mounted their relay to the engine compartment box - not on the engine.

Wires marked 87 & 30 should be at least 12 gage stranded.  Relay wiring can be 16 gage stranded.

Recommend:  Encase all wires with a proper wrap.  Solidly crimp or solder all terminals. Re-check everything!

Page 2 of 2

20-amp fuse