Table II.a      Comparison of Compressor Performance and Evaporator Type & Evaporation Temperature

|  | Evaporator | Compressor |
| --- | --- | --- |
| Type | Evaporation | Pressure | BD 50 | TFS4FK | NF9FX | SC21FX |
|  | Temperature | PSIG | PSIA | 12 volt | 1/8 hp | 1/4 hp | 1/2 hp |
|  | (F) |  |  | BTU/hr | Amps | BTU/hr | Amps | BTU/hr | Amps | BTU/hr | Amps |
| Evaporator Plate | 14 | 14.16 | 29.1 | 271 | 3.9 | 733 | 1.81 | 1639 | 3.66 | 2856 | 6.64 |
|  | 0 | 6.3 | 21.2 | 178 | 3.2 | 483 | 1.7 | 1112 | 3.6 | 1896 | 5.76 |
| Cold Holdover Plates | -10 | 1.8 | 16.6 | 126 | 2.74 | 341 | 1.62 | 811 | 3.45 | 1367 | 5.48 |
|  | -20 | -3.8 mm Hg | 12.9 | 87.8 | 2.32 | 237 | 1.56 | 589 | 3.32 | 991 | 5.32 |

Table II.b   Run Times of Various Compressors Depending on Evaporator Type & Evaporation Temperature

| Type | Evaporation | Compressor Run Time for 4000 BTU/day Cooling Load (hrs) |
| --- | --- | --- |
|  | Temperature (F) | BD 50 | 1/8 hp | 1/4 hp | 1/2 hp |
| Evaporator | 14 | 14.8 | 5.5 | 2.4 | 1.4 |
| Cold Holdover | 0 | 22.5 | 8.3 | 3.6 | 2.1 |
| Plate | -10 | 31.7 | 11.7 | 4.9 | 2.9 |
|  | -20 | 48.0 | 17.8 | 7.2 | 4.3 |

Notes:   1. Refrigerant R-134a.    2. Condensation temperature 105 F.     3. Liquid line temperature 95 F.

4. Evaporator superheat 5 F degrees.      5.  Suction line temp 60 F.