# SPECIFICATIONS for S/V: OCEAN FLIGHT

As at 31 May 2013

1995/1998

DESIGNER:	Dudley Dix of Dix Yacht Designs, South Africa

DESIGN:	DIX 43++    -  Centre Cockpit, Cutter Rig, Fin Keel, Scoop Stern

BUILDER:	G F Buckle of East Coast Yachts, Durban, South Africa

YEAR LAUNCHED:	1995 - 1998

REGISTERED:	Cape Town, South Africa

DIMENSIONS:

Material:	Steel (Radiused Chine – Round Bilge)

LOA:	13.6m / 44’

LWL:	12.17m

Beam:	4.1m / 13’5

Draft:	1.8m / 6’

Mast:	Paul Green 17.5m Aluminium

Fuel Capacity:	550lt

Water:	600lt ++

Displacement:	14.5 ton

Ballast:	4 tons lead

SAILS:										PURCHASED

Sail area – 322.31 sq.ft/ 89.83sq.m

Furling Genoa 130% - Doyle	Mar 1999

Main Sail, 4 Slab Reefing Points – Doyle	Sept 1999

Stack Pack – North Sails	Jan 2010

Spare Light Genoa (Ghoster)

Storm Jib

Stay Sail – Doyle	Nov 1998

Asymmetrical Spinnaker (Gennaker) – Doyle	Nov 1998

Dousing Sock – Doyle	Nov 1998

ANCHOR EQUIPMENT:

1 x Bruce Anchor – 45lb

30m x 10mm Chain

1x CQR 45lb Anchor

70m x 10mm Chain - minimum	Nov 1998

Windlass – Lofrans Tigres

Mooring Lines/ Warps and 5 Fenders

ENGINE / POWER:

Perkins 4236 – 72hp

Diesel engine

Cruising speed – 6.5 Knots at 1350 rpm

Consumption 1 gph

Batteries Starter -  Deltec 6V x 120 amp hr. x 2 = 200 Amp Hour	Feb 2009

Batteries House -  Deltec 6V 120 Amp hr. x 4 = 480 Amp hr.	Nov 2011

Battery Switch – Blue Seas	Nov 1998

Propeller – fixed 3 blade

Sump – approx. 8 lts

Bilge – approx.. 125lts

Alternator – 190 Amp	Nov 1998

Next Step Regulator	Nov 1998

Transformer (Shore Power Up) 220/110V	Nov 1998

Shore Power & Cable – Marenco	Nov 1998

Inverter Charger – Freedom 20/100 (200 watts/100 Amp Charger) 	Nov 1998

Wind Generator – Air Marine

Siemens Solar Panel – 50 watt

Siemens Solar Panel – 70 watt

INSTRUMENTATION:

Compass on Binnacle -  Plastimo 135	Nov 1998

GPS – Furuno GP-31	May 2000

ST-40 - Bi-Data – Raymarine	Jan 2007

ST-40 - Wind – Raymarine	Jan 2007

ST-60 - Repeater	May 2012

Heart Interface Link 2000 Manager for Inverter	Nov 1998

Radar – Furuno 1621	Mar 1999

SSB/Ham Radio – ICOM IC 725

Icom AT135 (Automatic Tuner)	Nov 1998

VHF – Navastar SM 5800

SAFETY EQUIPMENT:-  Class A Certificate of Fitness – more than 40nm offshore

Flares & safety equipment (Excluding Binoculars &	May 2013

EPIRB excl battery

6 safety harnesses

8 life jackets

6 man liferaft – Arimar Cannister Class 2 in s/steel holder – last serviced	May 2012

4 x CE approved Fire Extinguishers	May 2012

Jon Buoy

2 x Life Rings

1 x Self Lighting Life Buoy Light

STEERING:

Wheel (Rack and pinion/shaft actuation)

Aries Wind Vane

Autohelm ST6000 plus Autopilot	Nov 1998

Emergency Steering Tiller

WINCHES:

2 x 3 speed ASHAI 32 (Genoa Sheets)

2 x Barlow ST25 (Genoa & Main Halyards)

1 x Barlow ST19 (Main Sheet)

1 x Lewmar ST16 (Reefing Lines)

2 x Lewmar ST40 (Running Back Stays)

1 x Winch Handles

RIGGING:

Paul Green Mast & Boom

Mast Steps

Rigid Boom Vang

Harken Roller Furler 	Jan 2000

Stainless Steel Standing Rigging	Aug 2006

Running Back Stays

Double Spreader Rig

Deck Stepped Mast

DOMESTIC EQUIPMENT:

3 burner stove with oven and Grill – Force 10	Nov 1998

600 watt Microwave – Samsung	Nov 1998

Watermaker – PUR Survivor 160E – 25lt/hour	Nov 1998

Manual Toilet – Jabsco	Nov 1998

Pressurised Hot and Cold water (Heads & Galley)	Nov 1998

Pressurised Hot and Cold Transom Shower	Jan 2007

12V Frigoboat Keel Cooled Refrigeration, (Separate Fridge and Freezer)

Vacuum Cleaner

Handheld Duster Buster

TV Sansui	Jan 2007

DVD Player - Sansui 	Jan 2007

Stereo AM/ FM/ CD/ Tape – Alpine with 6 disc CD Changer	Nov 1998

Cabin and Cockpit Speakers	Nov 1998

2 x 10kg Propane Gas Bottles

GENERAL EQUIPMENT:

Bilge Pump – Electric

Henderson Bilge Pump -  Hand 25 GPM

Deck / Sea Water Pump

Gas Solenoid Valve & Alarm System – FONZ

5 x GEBO Hatches

5 x GEBO Opening Ports

Stainless Steel Roll bar with Davits	Oct 1999

COSMETICS /EXTRAS:

Varnished Beech Interior (Light Interior)	Oct 1998

3 Cabin Lay-out, extremely well ventilated

Blinds on all Side lights and Hatches – Kool Aluminium	Nov 2012

Halogen Lighting with Dimmers	Oct 1998

Stern Seats

Leather wrapped Steering Wheel	Oct 1998

Mosquito Screens 	Mar 1999

Sunbrella Dodger & Bimini	May 2009

Sunbrella full length Deck Awning 	Oct 1999

9’ Semi Rigid Dinghy – Caribe with Sunbrella Cover	Mar 1999

15hp Yamaha Enduro Outboard – Sunbrella Cover	Mar 1999

CONSTRUCTION:

Extremely strong rolled, welded steel hull in steel plate of 4 mm and up to 8mm, at point of stress.  Stainless steel transom.  Frames and floors in 8mm steel plate.  Full fin lead Ballast Keel of 8,816lbs / 4 tons.  Rod steering and universal ball joints.  Skeg mounted rudder.  Built in excess of ABS requirements.

ACCOMMODATION:

The interior is decorated in a modern manner, all counter tops are in a “corian” type resin mold as are the Heads.  The floors are all in “Floortex Flooring” which is reported to be stain proof.  Sleeps 6 in 3 double cabins.  1 Head and Shower. From forward – Chain locker with access from deck and forwarding cabin.  Forward cabin with large v-berth, followed by toilet, head and shower compartment.  Large saloon with settees to either side of a folding table.  The navigation table is then to starboard and galley to port.  Central steps lead to cockpit and then aft are 2 cabins, each with double berths.  Huge storage space, under all berths, and settees.  Huge full width lazarette (12’6) with sufficient space for 3 large Rubber Maid containers and 3 x 20lb gas bottles, the Aries, Outboard, diving bottle, etc.

REMARKS:

Ocean Flight is beautifully built of the highest quality materials, for example the galley lockers and drawers are fitted with surgical steel wire drawers on rollers, so each item is automatically stowed, when put away.  The yacht was originally built for the owner of her building yard and the detailing and finish are extraordinary.

A very safe, practical, self-sufficient, comfortable yacht for all Oceans!

Owner:  C.E. Douglass

Cell:  0828820034

Email:  ody@iafrica.com

SAS Registered:  South Africa

Price:  ZAR1 995 000.00