25/07/2015

Rigging / Rerigging Invoice found

30/07/18, 2108h

Oil change for engine done. Did NOT change oil filter. Oil Chnage for Saildrive done also but put in 10W-30 instead of SAE90. Need to rectify.

12/8/18, 2108h

Saildrive oil changed 3 times to SAE90

23/10/2018

Replaced corroded Exhaust Elbow

31/1/19, ????h

Water Pump reconditioned with new bearings. Impeller was good so not replaced.

2/4/19, 2390h

Oil Change - Yanmar Diesel Engine Oil SAE 30 CF-CF2

Oil Filter - LF 3462 Filter

Fuel FIlter 1 - FF 5260 Filter

Fuel Filter 2 - CAV 296

Both Belts Tensioned

Engine Degreased

3/5/19, 2430.2h

Keel Annodes Added

Saildrive Oil Changed

6/5/19

Port Lifelines replaced

Rear Lifelines replaced

3/6/19

Steering System Serviced

- Cables replaced

- Bearings Replaced

- Chain NOT replaced

6/7/19 2434h

Oil Change - Yanmar SAE 30

Oil Filter Change

Adjusted Valve Clearences

Reconditioned Heat Exchange system (cleaned and replaced seals)

Cleaned Exhaust Manifold (on inspection this was already quite clean)

Flushed Cooling System with Penrite 7 Year 450000KMs Green Coolant Premix

Replaced Exhaust Manifold Gasket

Replaced Exhaust Elbow Gasket

Replaced Timing Cover Gasket

Engine Degreased

20/2/2020

Antifoul - Ultra 2 in Dover White. Note there were some small signs of osmosis

SailDrive Service - Oil Change

16/07/2020 2468.9h

Oil Change - Yanmar SAE 30

Oil Filter Change

Inspected Fuel Filter - Looks perfect

Investigated slight fuel leak near fuel filter - tightened fuel filter and replaced copper crush washes

Tested Galvanic Isolator: 1072ma 1053ma on ground cable

8/1/21

Antifoul - Ultra 2 in Dover White, Trilux33 on Saildrive, Speedrpop on Propeller.

Note - Much of the fairing and paint fell of the keel, however it appears to be in good condition otherwise

Skins replaced: Head, Shower

New Rubber Boot for SD20 created and installed

SailDrive Service - Oil Change SAE90

17/7/2021 2551.0h

Oil Change - Yanmar SAE 30

Oil Filter Change

Air Filter Change

Fuel Filter 1 - FF 5260 Filter - Looked fine but replaced anyway

Fuel Filter 2 - CAV 296

Raw water pump impeller - Looked fine but replaced anyway

Replaced Rubber Hose - Heat Exchange Elbow (front of engine)

Replaced Rubber Hose - Heat Exchange to coolant pump (front of engine)

Replaced Rubber Hose - Heat Exchange to sea water (front of engine)

Replaced fuel hose from fuel filter to fuel lift pump (side of engine)

Replaced fuel hose from cav filter to fuel filter (side of engine)

Fixed slight oil leak from fuel pump by cleaning fuel pump shims and using Loctite 243 between shims (as recommended by manual)

Engine Degreased and washed

Found Gearbox Oil coming from between bellhousing of engine and upper gearbox of SD20. Suspect SD20 Lip Seal near the pinion gear is failing. Noticed that the oil was above the minimum mark. Dropped down to minimum mark to see if that makes a difference.

19/10/2021

Tested Galvanic Isolator: 0.843 and 0.856 volts for galvanic isolator test

Changed Filter in Hookah Air Breathing System

24/10/2021

Engine has been hard to start since last service. Fuel leaking from fuel filter. Took fuel filter out of boat and tightened fuel filter collar using vice. Also checked fuel filter timing and took photo.